California State Polytechnic University Pomona

Aerospace Engineering

ARO4080

FEM Documentation

for

Project 00

by

Todd D. Coburn

15 August 2020

Table of Contents

VOLUME I: FEM DOCUMENTATION REPORT

Table of Contents	iii

CHP	DESCRIPTION	PAGE

1.	Introduction	1-1

- Purpose	1-1

2.	FEM Documentation	2-0

- Sketch of Model	2-1

- Bulk Data File	2-2

- Material Properties	2-2

- Applied Loads	2-3

- Constraints	2-3

3.	FEM Results 	3-1

- Nodal Displacements	3-1

- SPC Forces	3-1

- Grid Point Force Balance	3-1

- Rod Element Forces & Stresses	3-2

4.	Assessment 	4-1

- Evaluation of FEM Results to Hand Analysis	4-1

APPX	DESCRIPTION	PAGE

A	FEM Lumping, Property & Material Hand Calculations	A-1

B	Hand Analysis Support	B-1

VOLUME II: F06 OUTPUT FILE

(separate file and volume)

VOLUME III: COMPLETE BDF LISTING

(separate file and volume – only provided when bdf is too large for Section 2.2)

1.0	Introduction

1.1	Purpose

The purpose of this report is to provide a template for documenting FE Models for ARO4080 Homework & Projects.  An example problem is documented herein to illustrate what information is required.

2.0	F.E.M. Documentation

2.1	Sketch of Model

The FEM is shown below.  This is a simple model requiring only a single sketch to shown its connectivity, loading, and constraint.  Additional sketches would have been included if needed for clarity.

.

Figure 2.1.1: FEM Sketch

2.2	Bulk Data File

The FEM bulk data file is shown below.

Notes:

- The font style & size is selected to show the bdf in a format similar to the text file it is stored in.

- For bdf’s of 5 pages or less, the entire BDF should be placed here.  For larger FEMS, only place an excerpt of the critical cards here, and provide the complete bdf listing as a separate file and volume.  Hardcopies of the separate volume should have formatting similar to this report.  In ARO4080, a separate text file with no special formatting but with the same filename, volume III, can be used.

$---------------------------------------------------------------------------

$ Prepared by: Todd Coburn

$ Date: August 15, 2018

$ Revised: 08/15/18

$ Title: Example 01-01

$---------------------------------------------------------------------------

SOL STATIC

TIME 5

CEND                       $ Designates end of Executive Control

ECHO = SORT

TITLE = ARO4080: Example 01-01 - CROD

LABEL = By Todd Coburn, 08/14/18

SUBCASE 1

SUBTITLE=Axial Force

SPC = 1

LOAD = 1

DISPLACEMENT=ALL

SPCFORCES=ALL

GPFORCE=ALL

STRESS=ALL

FORCE=ALL

BEGIN BULK                     $ Designates end of Case Control

GRID, 1,,0.,0.,0.              $ GRID,id,cord sys,x,y,z

GRID, 2,,10.,0.,0.             $ GRID,id,cord sys,x,y,z

CROD, 1,1,1,2                  $ CBAR,id,pid,grid 1, grid 2

PROD, 1,1,0.5,0.2,1.,0.1       $ PROD,pid,mid,A,J,C,NSM

MAT1,1,10.3E6,3.9e6            $ MAT1,id,E,G,v

FORCE,1,2,,10000.,1.,0.,0.     $ FORCE,id,grid id,cord sys,magnitude,i,j,k

SPC,1,1,123456,,2,2356         $ SPC,id,grid id,constraints,G1 disp,G2 id,G2

ENDDATA                        $ Designates end of Bulk Data section

2.3	Material Properties

This FEM is constructed on only aluminum elements.  This material is identified on a single MAT1 card, as follows:

MAT1,1,10.3E6,3.9e6            $ MAT1,id,E,G,v

The elastic & shear modulus for this material are shown.  Poisson’s ratio is computed by NASTRAN during runtime. Note: This section may appear overkill for simple FEM’s such as this one, but for larger models with more than 1 material, it is an important documentation step.

2.4	Applied Loads

There is a single 10 kip force applied at Grid Point 2 of this FEM, as shown on the FORCE card below.

FORCE,1,2,,10000.,1.,0.,0.

Note: This section may appear overkill for simple FEM’s such as this one, but for larger models with more than 1 applied load it is an important documentation step.

2.5	Constraints

There is a rather simple FEM with a single element.  The loading is axial as discussed in Section 2.4.  The FBD only needs a single reaction along the element at node 1 to react the applied load from load 2.  Yet NASTRAN, and many other FE codes require complete constraining of the FEM in order to keep the FEM from developing spurious rigid body motion.  Therefore, node 1 is completely constrained in all 6 degrees of freedom (dof), as shown in Figure 2.1.1, which is repeated as Figure 2.5.1 below.  Also, NASTRAN and many other FEA codes may require constraining of all degrees of freedom at every node, and since the rod has no lateral shear or bending stiffness, the 23 and 56 degrees of freedom may need constrained, as is done for this model.

SPC,1,1,123456,,2,2356

Note: This section may appear overkill for simple FEM’s such as this one, but for larger models with more than 1 applied load it is an important documentation step.

Figure 2.5.1: FEM Constraints

3.0	FEM Results

3.1	Nodal Displacements

Nodal displacements are summarized below.

Axial Force                                                         SUBCASE 1

D I S P L A C E M E N T   V E C T O R

GRID      COORDINATE        T1            T2            T3            R1            R2            R3

ID           ID

2            0      1.941748E-02  0.000000E+00  0.000000E+00  0.000000E+00  0.000000E+00  0.000000E+00

MAXIMUM DISPLACEMENT MAGNITUDE =  1.941748E-02  AT GRID 2

MAXIMUM ROTATION MAGNITUDE     =  0.000000E+00  AT GRID 2

EPSILON       =  0.000000E+00

STRAIN ENERGY =  9.708738E+01

3.2	SPC Forces

SPC forces are summarized below.

Axial Force                                                         SUBCASE 1

F O R C E S   O F   S I N G L E - P O I N T   C O N S T R A I N T

GRID      COORDINATE        T1            T2            T3            R1            R2            R3

ID           ID

1            0     -1.000000E+04  0.000000E+00  0.000000E+00  0.000000E+00  0.000000E+00  0.000000E+00

MAXIMUM SINGLE POINT CONSTRAINT FORCE MAGNITUDE  =  1.000000E+04  AT GRID 1

MAXIMUM SINGLE POINT CONSTRAINT MOMENT MAGNITUDE =  0.000000E+00  AT GRID 2

3.3	Grid Point Force Balance

The grid point force balances are are summarized below.

Axial Force                                                         SUBCASE 1

G R I D   P O I N T   F O R C E   B A L A N C E

GRID    COORDINATE   ELEMENT    SOURCE           T1            T2            T3            R1            R2            R3

ID         ID         ID

1          0          1            ROD   1.000000E+04  0.000000E+00  0.000000E+00  0.000000E+00  0.000000E+00  0.000000E+00

SPC FORCE  -1.000000E+04  0.000000E+00  0.000000E+00  0.000000E+00  0.000000E+00  0.000000E+00

TOTAL   0.000000E+00  0.000000E+00  0.000000E+00  0.000000E+00  0.000000E+00  0.000000E+00

2          0          1            ROD  -1.000000E+04  0.000000E+00  0.000000E+00  0.000000E+00  0.000000E+00  0.000000E+00

APPLIED LOAD   1.000000E+04  0.000000E+00  0.000000E+00  0.000000E+00  0.000000E+00  0.000000E+00

TOTAL   0.000000E+00  0.000000E+00  0.000000E+00  0.000000E+00  0.000000E+00  0.000000E+00

3.4	Rod Element Forces & Stresses

Rod element forces & stresses are summarized below.

Axial Force                                                         SUBCASE 1

F O R C E S   I N   R O D   E L E M E N T S

ELEMENT        AXIAL          TORQUE

ID           FORCE

1       1.000000E+04   0.000000E+00

Axial Force                                                         SUBCASE 1

S T R E S S E S   I N   R O D   E L E M E N T S

ELEMENT        AXIAL         TORSIONAL

ID           STRESS         STRESS

1       2.000000E+04   0.000000E+00

4.0	Evaluation

4.1	Evaluation of FE Results to Hand Analysis

It is good practice to perform a hand analysis before any FEM is attempted.  After developing the FEM, the results of both should be compared.  Note differences, and try to explain them.  Note similarities, and gloat.  Document what you find here.

A	FEM Lumping, Property & Material Hand Calculations

When preparing a FEM, there are often calculations to determine section properties and other aspects of the model.  This can be hand sketched and lettered, and should be placed here.  Sometimes it is useful to place these in section 2 as the properties & materials are introduced instead.

B	Hand Analysis Support

Before preparing a FEM, it is usually best to perform some rough cursory analysis of the structure and elements.  This should be done neatly, but can be hand sketched and lettered.  The result should be placed here.

References

[DLe5]	Daryl Logan.  A First Course in the Finite Element Method. 5th Edition.  Cengage Learning.  2012.